## Slide 1: Comparative Evaluation of Space Mean Speed Estimation Methods Using Trajectory Data and Edie’s Definition
Prepared by: Saurav Barua

## Slide 2: Work Plan
Location: Henri-Dunant Intersection
Methods:
Method 1: Entry-Exit travel time-based Space Mean Speed
Method 2: Instantaneous speed-based Space Mean Speed
Method 3: Trajectory based aggregation of Edie's Space Mean Speed

## Slide 3: Screen shot from video showing entry and exit gate

## Slide 4: Method 1: Entry-Exit travel time-based Space Mean Speed
Pseudo Code:
INPUT: vehicle-level dataset (Entry Time, Exit Time, Distance) STEP 1: Remove duplicate rows → keep one row per vehicle STEP 2: For each vehicle i: travel_time[i] = Exit_Time[i] - Entry_Time[i] STEP 3: Remove vehicles where: travel_time[i] <= 0 STEP 4: Compute speed per vehicle: speed[i] = distance[i] / travel_time[i] STEP 5: Convert speed to km/h if needed: speed[i] = speed[i] * 3.6 STEP 6: Compute Space Mean Speed (harmonic mean): SMS = N / SUM(1 / speed[i]) OUTPUT: SMS

## Slide 5: Method 2: Instantaneous speed-based Space Mean Speed
Pseudo Code
INPUT: trajectory dataset (Track ID, Time, Speed) STEP 1: Sort data by: Track ID, Time STEP 2: For each vehicle: Compute time difference: dt = current_time - previous_time STEP 3: Remove rows where: dt is NULL or dt <= 0 STEP 4: Convert speed: speed_mps = speed_kmh / 3.6 STEP 5: Compute step distance: step_distance = speed_mps * dt STEP 6: Aggregate per vehicle: total_distance[i] = SUM(step_distance) total_time[i] = SUM(dt) STEP 7: Compute per vehicle speed: speed[i] = total_distance[i] / total_time[i] STEP 8: Compute overall SMS: total_distance_all = SUM(total_distance[i]) total_time_all = SUM(total_time[i]) SMS = total_distance_all / total_time_all STEP 9: Convert to km/h: SMS = SMS * 3.6 OUTPUT: SMS

## Slide 6: Method 3: Trajectory based aggregation of Edie's Space Mean Speed

## Slide 7: Method 3: Trajectory based aggregation of Edie's Space Mean Speed
Pseudo Code:
INPUT:
trajectory dataset with:
Track_ID, Time, step_distance
intervals = [1, 2, 5, 10, ...]
road_length = max(cumulative_distance) - min(cumulative_distance)
FOR each interval T in intervals:
STEP 1: Create time bins
For each row:
time_bin = floor(Time / T) * T
STEP 2: Initialize storage per time_bin
For each time_bin:
total_distance = 0
total_time = 0
STEP 3: Aggregate trajectory contributions
FOR each observation (row):
total_distance += step_distance
total_time += Δt
NOTE:
Δt = 1 second (since data is 1 Hz)
STEP 4: Compute Edie variables per time_bin
flow (q):
q = total_distance / (road_length * T)
density (k):
k = total_time / (road_length * T)
space_mean_speed (v):
v = total_distance / total_time
STEP 5: Unit conversion
v_kmh = v * 3.6
STEP 6: Store results per time_bin
END FOR
STEP 7: Compute summary over all time bins
avg_flow = mean(q)
avg_density = mean(k)
avg_speed = mean(v_kmh)
OUTPUT:
- Time-bin level results
- Interval summary results

## Slide 8: Trajectory plots

## Slide 9: Comparison